## Slide 1: Redes de Computadores
Computer Networks
labs
1
Notes: 1
2012/2013
LEI - DI/FCT/UNL
Redes de Computadores

## Slide 2: Stop & Wait Protocol
Lab class 2
2
Notes: 2
2012/2013
LEI - DI/FCT/UNL
Redes de Computadores

## Slide 3: Summary
Brief overview of the Stop and Wait Protocol
The SW FTP Protocol
Study files: SwFtpPacket.java & SwFtpServer.java
Write and test: SwFtpClient.java
3

## Slide 4: Stop & Wait Protocol
Reliable, general purpose data transfer protocol
Breaks the file contents into DATA packets
Each data packet has a sequence number
The receiver uses ACKnowledge packets to tell the sender what it has received correctly up to now
Very simple — the sender only advances to the next data packet when it is sure the receiver received everything previously sent
4

## Slide 5: Stop & Wait Protocol
Sender:
Assigns to each data packet a (growing) sequence number
Sends the packet and installs an alarm. Then, if it receives:
  An ACK packet with the expected sequence number, it progresses to the next data packet
  An ACK packet with a wrong sequence number is ignored
  If the timer expires, it retransmits the last sent data packet
Receiver:
Whenever it receives a data packet:
  If the packet has the expected sequence number, keeps it, otherwise it is ignored
  Always sends an ACK packet with the sequence number of last correctly received packet
5
Notes: 5
2012/2013
LEI - DI/FCT/UNL
Redes de Computadores

## Slide 6: Stop & Wait File Transfer Protocol
6
This protocol transfers a file over UDP using the stop & wait protocol
It is a client / server application, where all initiative is with the client
It uses several different messages:
  To start the transfer (read file, write file, op codes 1 and 2)
  To send data packets (op code 3)
  To send ACKs (op code 4)
  To send errors (op code 5)
  To signal the file is finished (op codes 6 and 7)
All control messages (read, write, data, finalized) are ACKed
Sequence numbers of initial packets start at 0, the first data packet at 1

## Slide 7: Stop & Wait File Transfer Protocol Messages
op code
File name
0
op code=3
ip
header
udp
header
data: 0 up to Block Size bytes
seq number
seq number
op code=4
op code=5
Error message
error number
0
seq number
op code=6
Messages:
  To start the transfer (read file, write file, op codes 1 and 2)
  To send data packets (op code 3)
  To send ACKs (op code 4)
  To send errors (op code 5)
  To signal the file is finished (op code 6) or an ack of the receipt of this message (op code 7)
All control messages (read, write, data, finalized) are ACKed
Sequence numbers of the sent file start at 1
seq number
op code=7

## Slide 8: Some additional details
Op codes have 16 bits (short) and sequence numbers have 64 bits (long)
The sequence number corresponds to the position of the first byte of the data block in the file
The first byte of the file has sequence number 1
The sequence number of the ACK message corresponds to the position of the next byte to receive (the last byte well received + 1)
8

## Slide 9: Send File Example (Write)
op code = WRQ (write request), seq = 0
op code = DATA, sn = 1
op code = ACK, sn = 201
op code = DATA, sn = 201
op code = ACK, sn = 301
op code = FIN, sn = 301
op code = FINACK, sn = 301
op code = ACK, sn = 1
Client
Server
The initial request has sn = 0 and its ACK sn = 1
The first data packet has sn = 1, and has up to the byte 200 (200 bytes), its ACK has sn = 200+1
the second has sn = 201, and has up to the byte 300 (100 bytes), its ACK has sn = 300+1
The FIN packet has sn = 301 and its ACK has sn = 301 (the last well received byte + 1)
Notes: 9

## Slide 10: Get File Example (Read)
Client
Server
op code = RRQ (read request), sn = 0
op code = DATA, sn = 1
op code = ACK, block = 201
op code = DATA, sn = 201
op code = ACK, sn = 301
op code = FIN, sn = 301
op code = FINACK, sn = 302
The initial request has sn = 0 and its ACK, implicitly sn = 1, since it is ACKed by the first data packet
The first data packet has sn = 1, and has up to the byte 200 (200 bytes), its ACK has sn = 200+1
the second has sn = 201, and has to the byte 300 (100 bytes), its ACK has sn = 300+1 = 301
The FIN packet has sn = 301 and its FINACK sn = 300 + 1 = 301, the last well received byte

## Slide 11: The Stop & Wait Protocol is Robust
11
Sender
Receiver
Time
premature alarm expiration
ignored
duplicate
Data2 accepted
Data1,1
Data1 accepted
Data1,1
Data2,2
Data2,2
Ack,1
Ack,1
Notes: 11

## Slide 12: Goals of this Lab Work
Study file SwFtpPacket.java
A simple server is available: SwFtpServer.java
Build a client able to send a file to this server
12